The University of Queensland
School of Earth and Environmental Sciences
An Introduction to Finite Elements
With Application To Gravity Fields
Lutz Gross
E-mail : l.gross@uq.edu.au

---
Objective: Geophysical Imaging
- constructing a 3D map of subsurface from from surface or near surface observation
  - For instance: density ρ from vertical gravity gz
- This process is called inversion
  - Key step: forward model
    - calculate vertical gravity gz at the surface from an estimated density distribution ρ

---
Geophyscial Imaging (cont.)
Example from Western Queensland
Given Data: vertical
gravity anomalies gz at surface
Recovered 3D map:
surface density ρ

---
 Gauss’s law for gravity
- Gravity field g=(g0,g1,g2) due to density ρ needs to fulfill:
- Coordinate system x=(x0,x1,x2):
  - x0,x1 horizontal
  - x2=z vertical

---
Potential Field
- gravity field is a conservative field:
- Hence gravity field g the negative gradient of the so-called gravity potential u

---
PDE for the Potential
- Partial Differential Equation (PDE) for the potential u
- Spelled out in 2D: x0 horizontal, x1 vertical
- left( {partial^2 u } over {partial x_0^2} + {partial^2 u } over {partial x_1^2} right) = - 4 %pi G %rho

---
Anomalies

---
Background gravity
- Common approach in geophysics:
  - Eliminate the background field and properties from the problem → looking at anomalies
  - Based on a ‘homogeneous half-space’ solution
Background model constant density + air layer
Residual model

---
Residual Model
- Assume bounded domain
- Homogeneous boundary conditions

---
Boundary conditions
- Dirichlet-type boundary conditions on ΓD
  - ΓD = top of the domain Ω
- Neumann-type boundary conditions on ΓN
  - Outer normal field n
    - Set normal component of gravity field g to zero
  - ΓN = all other faces of the domain Ω

---
PDE we need to solve
- Make life easy: drop the ‘
- PDE for gravity potential u on domain Ω:
- plus boundary conditions.

---
Finite Element Approximation
Idea: approximate the solution u by function uh that is
  1. continuous
  2. piecewise linear
  3. solves the PDE (somehow)
solution u
approximation uh

---
It all starts with a Grid
row i1
E=(i0,i1)
column i0

---
Grids
- Subdivide the domain into an array of elements arranged in N1 rows and N0 columns
  - A total of N1 N0 elements, and
  - A total N=(N1+1)(N0+1) nodes
- The set of all these nodes:

---
Elements
- The set of elements is an unordered list
- An element is described by the node ids of its vertices:
{ }

---
FEM Approximation
- FEM approximation is a linear combination of the FEM basis functions ϕph with p=0,…, N-1
- Unknown coefficients Uph
- basis function ϕph is associated with node p

---
FEM Basis Function
Properties of basis function ϕph
Continuous function
Value one at node p
Value zero at all other nodes q≠p
Linear function on each element
Hence: it is identical zero on all elements that do not contain node p as vertex
At Node p
ϕph
x1
x0

---
Duality
- There is a duality of basis functions and nodes
- Hence: coefficient Uph is the value of the FEM approximation at node p:

---
Some Notations
- Vector of node values Uh:
  - Component of Uh called degrees of freedom (DOFs)
- arrange the basis function as a vector:
- FEM approximation in a convenient way

---
Basis Function on an Element
- On element E basis functions are bi-linear polynomial
    - x0,x1 in element E,
- a,b,c and d are suitable factors depending on node p and element E
  - Determined by the duality condition!
- Note: a=b=c=d=0 if node p is not in element E

---
Local Basis Functions
- Local basis function = part of the global basis function on an element
  - Obviously: we are looking at non-zero part only
  - Here: four local basis functions N0, N1, N2, N3:
N0 @E=(2,2)
N0 @E=(1,2)
N2 @E=(1,1)
N4 @E=(2,1)

---
Local Basis Functions
- For square element with edge length h and left-lower corner c=(c0,c1)
- Task: Check duality with the four vertices (c0,c1), (c0+h,c1), (c0,c1+h), (c0+h,c1+h)

---
The FEM Solution
- Motivation: get the FEM approximation uh with the best gravity approximation:
- in the root means square (RMS) sense:

---
Condition for FEM solution
- Apply `	virtual displacement`:
  Perturb solution uh by small increment vh=ϕph for any node p:
- Then we have for any α :

---
A bit of calculus:
α

---
FEM Solution
- So FEM uh needs to fullfil this condition for all basis functions vh=ϕph
- But we don’t know the solution u ?
  - Somehow we need to use:

---
FEM Solution (cont.)
- Split integration over domain into integration over elements individual E:
- apply Green’s first identity on each element

---
FEM Solution (cont.)
- Insert PDE:
- Two elements E1 and E2 with touching faces have normal n1 and n2 with opposite signs:
- Hence: as vh is continuous across element edges:

---
Boundary conditions:
- Neumann-type boundary conditions on ΓN
- Dirichlet-type boundary condition on ΓD
  - Only use vh=ϕph with node p not in ΓD
u=0 " on " %GAMMA_D toward "only use " v^h " with " v^h=0 " on " %GAMMA_D

---
Condition for FEM Solution
- Putting it all together:
  - Find uh that fulfills the following conditions
    - Meets the Dirichlet boundary condition: uh=0 on ΓD
    - For all vh with vh=0 on ΓD :

---
System of Linear Equations
- Recall:
- Dirichlet condition ‘uh=0 on ΓD ‘ translates:
  - If node p in ΓD then
eg. all nodes localeted at the top face of the domain

---
System of Linear Equations (cont.)
- With vh=ϕph for node p not in ΓD
- This is a system of
  - N equations: one at each node
  - N unknowns = values of uh at the nodes

---
Compact form
- In compact form this is
- With (ignoring Dirichlet Boundary conditions):

---
Matrix Structure
- Sh is called stiffness matrix
- Entries can be obtained element-by-element
  - Hence: Shpq is zero if there is no element E that has node p and q as a vertex.

---
Matrix Structure (cont.)
- The stiffness matrix is sparse
  - The number of non-zero entries is small compared to the size of the matrix

---
Sparsity
- Use special compressed formats such as
  - compressed sparse row (CSR): stores value + column index
  - dictionary of keys (DOK): stores value + (column, row) index
- For our case:
  - Size of full matrix N2
  - Number of non-zeros: about 8 N
    - As each node has maximum of 8 neighboring nodes connected via an element.
  - For a 100x100 grid:
    - Sparsity < 0.08%
    - Savings of memory for CSR format: around a factor 600

---
Numerical Properties
- The stiffness matrix is
    - Symetric:
    - Positive definite:
  - See lecture nodes for details
- Solution methods for the linear system:
  - Direct method: Sparse LU factorization
  - Iterative method: Conjugate Gradient method

---
Matrix Assemblage
- The matrix and right-hand-side is build up on an element-by-element base.
  - This can be done in any order!
- We need an enumeration of the global nodes
  - Determines the sparsity pattern of non-zero entries in the stiffness matrix
    - Is impacting on computational performance and memory requirements

---
Node Enumeration
- Here we use a grid row-by-row scheme:
  - First count along the x_0 axis and secondly along the x1-axis:
  - Lower, left corner:
    (i0,i1)=(0,0): n=0
  - Upper right corner:
    (i0,i1)=(N0,N1): n=N0 N1-1
i1
i0

---
Example
Element E=(i0,i1)

---
Local Element matrices
Evaluate the local version of the PDE using the four local basis functions N0, N1, N2, N3:

---
Add to Global Stiffness matrix
- Recall the connection between local and global basis functions:
- This tells us where to add the local element matrices:

---
Get the local element matrices ..
- Assume: density ρ is constant in each element
  - Density is given as an array:
- We know the local basis functions so the integrals can be calculated analytically
  - They are scaled version of element matrix for edge length h=1.

---
Element Matrices for Gravity
For element E with
edge length h
edge length h=1

---
Dirichlet-Type Boundary condition
- Once the the stiffness matrix is assembled eliminate rows corresponding to nodes p with Dirichlet-Type boundary condition.
- Simplest way: overwrite row p with equation:
- That is:

---
Gradient Calculation
- Gradient of FEM solution is not continuous.
- calculated at element centers mE:
Collects values given at FEM nodes
at the element vertices

---
Gradient Calculation (cont.)
- Again this can be relayed back to local basis function on an element with edge length h=1:
- And then:

---
Pseudo program
1. Initial stiffness matrix S and right hand side b
2. for all element E
  1. Calculate local element matrices SE, bE
  2. Add SE, bE onto S and b
3. Overwrite equations for Dirichlet conditions in S and b
4. Solve AU=b
5. Return FEM solution U at FEM nodes.